## Slide 1
SMART POSTURE CORRECTION SYSTEM
CB.AI.U4AIM24007- ARNITA N CB.AI.U4AIM24021- THANMAI SAI K CB.AI.U4AIM24035- SAI PRANAVI R CB.AI.U4AIM24040- SHREENIDHI G
FACULTY :
Dr. SnigdhaTanu Acharya
Dr. Amrutha V
Introduction to NN, CNN and GNN (24AIM113) & Analog System Design (24AIM114)
01
TEAM MEMBERS :

## Slide 2
02
STRAIGHT UP:
This is designed to monitor and classify back posture using an MPU6050 IMU sensor and an ESP32 microcontroller.
Components used:
1. ESP-32 microcontroller
2.MPU 6050
3.Vibration motor
4.Belt

## Slide 3
03
SI.NO. | Challenges Encountered | Solution
1. | We faced a problem in finding the suitable board for ESP32 in the Arduino IDE. | We are able to figure it out from Github links, Sent by lab assistant.
2. | We faced a problem in selecting suitable IMU sensor whether it is MPU6050 OR MPU9050. | The MPU9050 includes a magnetometer in addition to the 6-axis accelerometer and gyroscope, which is not required for our project. Therefore, we chose the MPU6050.
3 | We were unable to connect the ESP32 to the Arduino IDE via Bluetooth. | For now we are using USB cable in place of bluetooth connection.
PROBLEMS FACED:

## Slide 4
04
Sensor Position | Angle | Good Posture Range | Bad Posture Range
Upper Thoracic | Pitch | -5° to +5° | > +15° (Forward Slouch)
Upper Thoracic | Roll | -3° to +3° | > ±10° (Lateral Lean)
Right Shoulder | Roll | -3° to +3° | > +8° (Shoulder Hike)
ANGLES:
STEP 2: HOW TO CALCULATE ANGLES
STEP 1: RANGE OF VALUES FOR CATEGORY
For forward /backward leaning:
For side-to-side leaning:
Pitch=
Roll=
Gyroscope data- for inclination angles:
Source: Malik, Nayyer Nayab, M. Javed Hyder, and Ajmal Shah. "EXPERIMENTAL INVESTIGATION ON TECHNIQUES TO IMPROVE THE ACCURACY OF MPU 6050 FOR TILT MEASUREMENT." JOURNAL OF HARBIN INSTITUTE OF TECHNOLOGY 54.9: 2022.
Complementary Filter:
  Low-pass filter: Reduces accelerometer jitter.
  High-pass filter: Minimizes gyro drift.
  Fusion: Combines both for realistic output.
The complimentary filters iteratively update the Euler angles by the following formulas:

## Slide 5
05
Feature | Acc1_X | Acc1_Y | Acc1_Z | Gyr1_X | Gyr1_Y | Gyr1_Z | Acc2_X | Acc2_Y | Acc2_Z | Gyr2_X | Gyr2_Y | Gyr2_Z | Pitch | Roll | Posture Type
1 | 9.07 | -1.06 | 4.32 | -0.08 | -0.03 | 0.02 | -3.54 | -2.77 | 7.41 | -0.07 | 0.02 | -0.01 | 2.50 | -1.20 | Good
2 | 6.94 | 3.21 | 6.34 | -0.03 | -0.01 | -0.01 | -7.23 | 3.36 | 4.25 | -0.05 | 0.03 | -0.01 | 18.00 | 12.00 | Bad
POSTURES:
GOOD
BAD
  Forward Slouch: Pitch angle greater than +15°.
  Backward Slouch: Pitch angle less than -15°.
  Side-to-Side Slouch: Roll angle greater than ±10°.
  Pitch angle between -5° and +5°
  Roll angle between -3° and +3°

## Slide 6
CIRCUIT DIAGRAM
https://wokwi.com/projects/422158056135560193
06

## Slide 7
07
Data collection:
  No of people =5
  No of samples = 2000 (1000-good posture,1000-bad posture)

## Slide 8
08
DATA SET OVERVIEW:
Labels:
0→ Good Posture
1→ Bad Posture

## Slide 9
09
NEURAL NETWORK:
  We are using the most basic type of artificial neural network Feedforward Neural Network (FNN) to train our dataset .
DATA PREPROCESSING:
  Handle Missing Values
  Feature Normalization
  One-Hot Encoding of Labels
  Split Data into Training & Testing Sets
  Shuffle the Data

## Slide 10
10
HYPER TUNING PARAMETERS:
EPOCHS VS LOSS:
ACCURACY AND LEARNING CURVE: